## Slide 1: Gamma Ray and Anti-Matter Survey (GRAMS)
Power Distribution Unit (PDU)
Time Projection Chamber (TPC) SiPM Low Voltage Board

## Slide 2: Agenda
The Power Distribution Unit (PDU) for GRAMS is extensive
  Only reviewing the Low Voltage Board within the SiPM Box
Purpose of the Board
Block Diagram
Schematic Review
Grounding Configuration
Layout Review

## Slide 3: Board Power
Recalling from the SiPM Box, there is a board that is providing +5V and +12V for telemetry and drive for the on-board DC-DC Converters
  This can be utilized to run the SiPM LV Board as well.

## Slide 4: Block Diagram of TPC SiPM Box
The S1 through S6 along with the Telemetry PDU Board were reviewed previously
  The SiPM LV Board will also reside in this box. This review is only pertaining to that box.
S1
S6
+12VIN
+12VRTN
=
=
+5V
+5VRTN
6 SiPM
& SiPM LV PDU
SiPM LV Board

## Slide 5: Schematic Review of SiPM LV Board

## Slide 6: On-Board DC-DC Converters
The rails that this board provides to the cold SiPM preamplifiers are +2.5 / -5.0V
  This is achieved by using two converters from the same family that provide different voltages.
    PDQ10-Q24-S5-D (5V Rail)
    PDQ10-Q24-S3-D (3.3V Rail)
      Trim resistor pads are provided if that becomes a need
    Output voltages are isolated.

## Slide 7: Power Rails
The SiPM LV Board receives +12V and +5V that drive the DC-DC Converters and Telemetry, respectively.
  This diagram also shows the grounding configuration

## Slide 8: Input EMI/EMC Network
EMI/EMC Network is consistent with other designs that use the same CUI Converters of this class
  Switching Frequency: 280kHz for all PDQ10-Q24’s
  Input Network FC = 29kHz, ZIN = 0.55W
    ZIN(U3) = 80W

## Slide 9: Enable / Disable Circuitry
PDQ10-Q24-S(x)-D Enable Signal
  There is a 10kW Pull-Up resistor internal to the Converter that defaults the block to enabled if no external control circuitry is added.
  Am using an opto-coupler to control this function
  ISP281D:
    Current Transfer Ratio (CTR): 300 to 600%
    ID = 100nA
    ISAT = 60 to 120mA
Truth Table |  | 
SiPM_LV_Enable | Low | High
Enable Line | Low | High
DC-DC Conv. | Disabled | Enabled

## Slide 10: Telemetry Points
Telemetry points are output on J5 (15-Female, HD DSUB)
  +2.5V Voltage and Current Monitor
  -5V Voltage and Current Monitor
  Temperature Monitor

## Slide 11: LED Indicator
Part Num: SSI-LXH072GD
Mounted on Chassis
1-1123824-1
1-1123823-1 mates to the 1-1123824-1
Easy to mate and de-mate

## Slide 12: Layout Review of SiPM LV Board

## Slide 13: Layer Definition and Stack-Up
10 – Layer Board
  Layer 1: Routing
  Layer 2: Secondary Power RTN
  Layer 3: Secondary Telemetry RTN and CUI Converter RTN
  Layer 4: Secondary PWR IN
  Layer 5: Secondary PWR RTN
  Layer 6: Secondary Telemetry RTN
  Layer 7: +2.5V Plane, CUI Input PWR
  Layer 8: -5V Plane, CUI Input RTN
  Layer 9: Secondary PWR RTN
  Layer 10: Chassis GND
Board Fab House: Sunstone Circuits
  Standard 10-Layer Stack up
Not expecting high currents or any high-speed signals