## Slide 1: Polsir IPDU Isolated Design Discussion

## Slide 2: Overview of Ground Loop Risk to Polsir Design
Multiple tie points to chassis in the system and a single shared return produce ground loops, a design risk that can introduce noise and adversely impact sensitive instruments.
In the Polsir system, returns are tied to chassis in multiple places (input power source, S-band antenna, polarimeters)
  Multiple connections to chassis and a shared return create loops (called ground loops) that can pick up noise and allow extraneous current flow in the system
  This noise/current through chassis can impact sensitive measurements and damage electronics
The IPDU can reduce these risks by implementing isolation in the design

## Slide 3: Ground Loops
Simplified System Diagram
Associated Design Risks
The loop through the return and chassis forms an antenna
  EM fields can induce current in the loop, introducing AC noise into the system
  A large EM pulse can cause a current spike and damage the electronics
The two chassis connection points may not have precisely the same ground voltage
  This can cause a current flow that introduces an error in measurements
Ground Loop Illustration

## Slide 4: Isolated Design Solution
In this isolated design, there is no path for a ground loop between the input and output

## Slide 5: Our System
Polarimeters require close ties to chassis due to high frequencies
Vadir has sensitive electronics (24-bit ADC, 16-bit requirement); precise measurements are needed
Polarimeters share frequency bands with S-band antenna, which may increase susceptibility to chassis noise damage
Motor generates EM fields, which couple with RTN-chassis loop antenna, and generate chassis noise
S-band antenna requires close ties to chassis due to high frequencies

## Slide 6: Input-Output Isolated System Solution
Polarimeters, Mini-Z, and Vadir share a return
Battery, motors, and the S-band antenna share a return
There are still ground loops on the input side and on the output side, but not across input to output
Noise generated by the motors and battery is kept away from sensitive electronics on Vadir and the polarimeters, at the cost of a second PCB and reduced PDU efficiency
Two conversion stages are needed, requiring a second PCB and reducing overall PDU efficiency (~4.7W additional dissipation)

## Slide 7: Isolated Design Impacts
Benefits
An isolated design of the PDU can keep noise on the input side away from sensitive electronics and measurements on the output side
  Ground loops within the input and output sides of the system would remain, but the overall risk is reduced
Drawbacks/Considerations
A second PCB is required for the isolated converter stage, impacting cost and schedule
PDU dissipation increases by approximately 4.7W
  Currently investigating whether BCT can accommodate the increased power draw
All numbers shown are approximations
Including an isolated stage in the PDU significantly improves the design overall, but has impacts on the power budget, cost, and schedule

## Slide 8: Backup Slides

## Slide 9: Grounding Diagram