## Slide 1: GRAMS PDU Description
Dave Durachka, Code 564

## Slide 2: List of Sub-Systems in the PDU
Cold Time-Projection Chamber
  Houses the SiPM Power Boards (x6), the SiPM Pre-Amplifier, Charge Pre-Amplifier, as well as Telemetry Power Boards
  The High Voltage Board Inside the pressure vessel is also part of the Cold TPC section.
Warm Time-Projection Chamber
  Houses the Shaper Power board, as well as the data acquisition power boards
CPU
  Hub CPU and DAQ CPU power boards are housed here
Time of Flight Section
  This houses the Time-Of-Flight Power Board.

## Slide 3: Design Philosophy
Each of the sub-systems will be powered from a single DC-DC Conversion done on the Main PDU Box. This box will receive the +28V from the battery pack on the balloon gondola and convert down to +12V that will drive each Sub-System’s PDU Board.
  Each sub-system will have a dedicated power board that will receive the +12V and convert down or up to the prescribed value needed for the sub-system.
  Requirements have been captured for the PDU system and agreed to by everyone.
  An Interface Control Document (ICD) will accompany this presentation to provide completeness to this design.

## Slide 4: Harnessing Nomenclature
Classes of Harnessing
  Input Power Cables to the PDU (Preceded with a P) at the box level
  Telemetry Cables within the PDU (Preceded with a T) at the box level
  Cables providing power From the PDU (Preceded with a J) at the box level

## Slide 5: COLD TPC PDU

## Slide 6: Cold TPC SiPM Bias Power Board
The Image to the left is describing the board providing power for both the SiPM Bias as well as the telemetry section of the SiPM Bias Board.
  J2 – J7 will provide +12V and +5V to each SiPM Bias Board.
  This board will receive +12V from the Main DC-DC PDU Board.

## Slide 7: Cold TPC SiPM Bias Board
The SiPM Bias Board is shown to the Right.
  J1 and J2 receive the +12V and +5V (with returns) respectively.
  J3 is the command / control, and telemetry portal to this board.
  U1 is the 1/16A12-P4-I5 converter manufactured by Ultravolt and will provide the prescribed voltage rail to each SiPM within the Cold TPC Section.

## Slide 8: Cold TPC SiPM Bias Box Diagram
Chassis
W-100
W-101
W-102 - 104
W-105 - 107

## Slide 9: Cold TPC SiPM Bias Box Design

## Slide 10: Cold TPC Charge and SiPM Pre-Amp Power Board
The image to the left describes the power board providing +/- 5V for the telemetry sections of the PDU Boards servicing the Charge and SiPM Pre-Amplifier Sub-Systems

## Slide 11: SiPM Pre-Amplifier Board
The Image to the Right is showing the SiPM Pre-Amplifier PDU Board.
  J1 receives +12V from the Main PDU Board
  J2 receives the +/- 5V from the Charge and SiPM Pre-Amplifier Board shown in the previous slide.
  J3 Provides the telemetry from this board.
  J4 and J5 deliver +2.5 / -5 respectively to the load.

## Slide 12: Charge Pre-Amplifier Board
The image to the right is showing the Charge Pre-Amplifier PDU Board
  J1 is receiving the +12V from the Main PDU Board
  J2 is receiving the +/- 5V from the Charge and Pre-Amplifier Power board
  J3 is providing the telemetry from this board
  J5 and J4 are providing the +/- 5V to the Load.

## Slide 13: Cold TPC Charge and SiPM Pre-Amp Box Diagram
Charge Pre-Amplifier PDU Board
SiPM Pre-Amplifier PDU Board
SiPM and Charge Pre-Amp Power Board
P2
P3
P4
T3
T4
J1 (Secondary PWR)
J2 (Telem power)
J3 (Telem)
(+5V) J5
(-5V) J4
8
+/- 5V
8
+/- 5V_RTN
+12V
+12V_RTN
12
Telemetry Values
J1 (Secondary PWR)
J2 (Telem power)
J3 (Telem)
(-5V) J5
(+2.5V) J4
8
+/- 5V
+/- 5V_RTN
8
+12V
+12V_RTN
15
Telemetry Values
J7
J8
J9
J10
To Load
To Load
To Load
To Load
* All harnessing called out in this drawing are Twisted Pair
W-110
W-112
W-111
W-113
W-114
W-115
J1 (Secondary Power)
(+/-5V Telemetry PWR) J2
(+/-5V Telemetry PWR) J3

## Slide 14: High Voltage Bias (-10kV) for Cold TPC
Images to right show the HV PDU board for the Cold TPC
  J1 and J2 receive the main input power of +12V. The pinout orientation are identical, swapping these will not harm anything.
  J3 is the Telemetry I/O
  J4 provides a means to configure he onboard DAC and provide the enable signal. This board will reside in its own box.
DC-DC Converter resides on bottom of the board

## Slide 15: WARM TPC PDU

## Slide 16: Warm TPC Boards
The Warm TPC PDU has four boards associated with it
  DAQ +3.3V
  DAQ +/- 5V
  DAQ +12V
  The Shaper
The Shaper is a larger board and can be put into its own box, it also doesn’t interact with the other boards as part of the PDU design.
All of the DAQ boards are meant to work with each other and should be part of the same box.

## Slide 17: CAEN-NEVIS DAQ PDU Box Diagram
J1 (+5V for Telemetry Rail)
J4 (Telemetry)
J2 (Secondary Power)
J2
To Load 3.3V
To Load 12V
J3
(+5V for Telemetry Rail)
J4
J2 (Telemetry)
J1 (Secondary Power)
J4
J5
To Load +5V
To Load -5V
J6
(Telemetry Power Rails)
+5V +5V RTN
+5V +5V RTN
+/-5V +/-5V RTN
J2 (Secondary Power)
J3 (Secondary Power)
J1 (Telemetry, CMD/CTRL)
8
13
8
P5
P6
T5
T6
9
8
P7
8
T7
8
P8
W-120
W-121
W-122
W-129
W-123
W-124
W-125
W-126
J11
J12
J13
J14
TP-1

## Slide 18: CAEN-NEVIS +/- 5V PDU Board
The +/- 5V Board is to the right. The top portion of the board is supplying the power to the sub-system load.
  The +5V rail is spec’d at 8.5A
    42.5W
  The -5V rail is spec’d at 1.993A
    9.9W
  Both converters are the VHB75W-Q24-S5 and can supply up to 75W.
The total input power with these levels is ~ 60W for this board.

## Slide 19: CAEN-NEVIS +12V Board
The +12V CAEN-NEVIS PDU Board is to the left.
  The +12V supply is spec’d to pull 1.993A
    23.9W
  The converter on this board is the PDQ30-Q24-S12-D, which can provide 30W.
The input power on this board will be 26.5W

## Slide 20: CAEN-NEVIS +3.3V PDU Board
The CAEN-NEVIS 3.3V PDU Board is to the right.
  This rail is spec’d to supply 12.1A to the load.
    40W
  The converter on this board is the VHB75W-Q24-S5 and can supply up to 75W.
The input power for this board will be ~ 45W.

## Slide 21: Shaper PDU Box Diagram
J2 (Secondary Power)
J1 (Telemetry, CMD/CTRL)
P9
T8
J15 (Telemetry Power Rail from TP-1 Connector)
TP-2
To Load +3.3V
To Load -3.3V
J15
J16
J4
J3
To Load +3.3V
To Load -3.3V
J17
J18
J6
J5
To Load +3.3V
To Load -3.3V
J19
J20
J8
J7
To Load +3.3V
To Load -3.3V
J21
J22
J10
J9
To Load +3.3V
To Load -3.3V
J23
J24
J12
J11
To Load +3.3V
To Load -3.3V
J25
J26
J14
J13

## Slide 22: The Shaper Board
The shaper board is providing 6 pairs of +/- 3.3V rails.
  The total power being pulled on the +3.3V rail is 1.485W
  The total power being pulled on the -3.3V rail is 1.485W
    At this power, the converters are approximately 80% efficient.
  Pin ~ 1.9W each.

## Slide 23: FLIGHT Computer PDU

## Slide 24: CPU PDU Board
The Flight Computer is supplying power to several separate loads. The PDU board is shown to the right.
  The different sections of this board are outlined by the top-level metal down to the bottom layer, all connected to chassis. This is to not only delineate the circuits, but to handle any noise issues that may arise.
  This board should have its own box.

## Slide 25: CPU PDU Power Dissipation
Sabertooth PDU
  Uses the PRC60-24-S12 for conversion, capable of 60W
    Input power estimate: 55.3W
Sabertooth I/O PDU
  Uses the PRC60-24-S12 for conversion as well
    Input power estimate: 44W
PCIe Bifurcator PDU
  Uses the PRC60-24-S12 for conversion as well.
    Input power estimate: 39.5W
SSD & HUB PDU
  Both use the PDQ30-Q24-S5-D converter, capable of 30W.
    SSD: 5.8W || HUB CPU: 6.2W
      Total Power Input: 12W
Sabertooth PDU
  +12V, 4.2A
    50.4W
Sabertooth I/O
  +12V, 3A || +5V, 100mA +3.3V, 500mA
    38.15W
PCIe Bifurcator PDU
  +12V, 3A
    36W
SSD PDU
  +5V, 1A
    5W
HUB CPU PDU
  +5.5V, 1A
    5.5W

## Slide 26: CPU PDU Box Diagram
J1 (Secondary Power) Sabertooth PDU
J2 (Secondary Power)
PCIe Bifurcator PDU
J4 (Secondary Power)
SSD PDU
J7 (Telemetry CMD/CTRL)
J5 (Secondary Power)
Telemetry Power
J3 (Secondary Power)
Sabertooth I/O PDU
J13 (Secondary Power)
Hub Computer PDU
(Sabertooth PWR) J18
(PCIe Bifurcator PWR) J17
(SSD PWR) J6
(Sabertooth I/O PWR) J16
(HUB Computer PWR) P1, P2
P10
P11
P12
P13
P14
P15
J27
J28
J29
J30
J31
T9
T10
T11
(Current Telemetry) J14
(Voltage Telemetry) J15

## Slide 27: Time-of-Flight PDU

## Slide 28: Time of Flight
The TOF PDU is shown to the right.
  This rail is spec’d to pull 4A @ 12V
    48W
  Using the VHB75W-Q24-S12 converter to provide the +12V
    Capable of 75W, with h = 83%
    Input power estimate: 57.9W

## Slide 29: TOF Box Diagram
J1 (Secondary Power)
J2 (Secondary Power)
J3 (Telemetry CMD/CTRL)
J32
+12V To Load
P16
P17
T10

## Slide 30: Total Power Draw
Total Power Demand on Main DC-DC Converter Box |  | 
Sub-System | Power Demand | Units
Cold TPC | 42.01 | Watts
Warm TPC | 141 | Watts
CPU | 160 | Watts
TOF | 60 | Watts
Total Power Needs | 403.01 | Watts
Current Draw @ 12V | 33.6 | Amps
Would suggest we look at the QSB40024S12 converter by XP Power
  Can supply +12V @ 400W
    Can use two in Parallel

## Slide 31: Backup Slides

## Slide 32
Main DC-DC
Converter Board
+28V
+28V RTN
=
+12V
+12V RTN
=
Power
Return
Chassis
Cold TPC PDU Section
SiPM Bias Boards (x6)
SiPM Pre-Amp & Charge Pre-Amp
-10kV HV PDU
Warm TPC PDU Section
Caen/Nevis DAQ
Shaper
Flight Computer
HUB and DAQ Computer PDUs

## Slide 33
SiPM Bias Boards (x3)
SMA Bulkhead
J1
J2
J3 - Telemetry
+12V
+12V
+12V_RTN
+12V_RTN
+5V
+5V_RTN
+5V_RTN
J2 – J4
SiPM Bias Board
and Telemetry Power
(x1)
J1
To Load
P1
J1-J3
24
T1
SiPM Bias Boards (x3)
J1
J2
J3 - Telemetry
J5 – J7
+5V
+5V_RTN
+5V_RTN
+12V
+12V
+12V_RTN
+12V_RTN
T2
SMA Bulkhead
To Load
24
J4-J6
SiPM Bias Box (Cold TPC) Wiring Diagram
TP
TP

## Slide 34: Warm TPC

## Slide 35
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
1
6
2
7
4
8
5
9
Chassis
1
6
2
7
4
8
5
9
Chassis
1
6
2
7
4
8
5
9
Chassis
Chassis
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
NorComp Inc. 171-025-103L001
25-Pin D-sub Panel Mount
NorComp Inc. 977-025-020R121
25-Pos Back-shell
x
Würth Elektronik
61800924823
9-Pin D-sub
In-Line Connector
Würth Elektronik
61801525311
9-Pos Back-Shell

## Slide 36
Telemetry Power Board
SiPM Bias Board
Telemetry Power is connected to J1 and J2 of the SiPM Bias Board

## Slide 37
1
2
3
4
5
6
7
1
2
3
2
1
4
3
TP
+5V RTN
+5V RTN
+5V
+12V RTN
+12V RTN
+12V
+12V
TP
Phoenix Contact 1803471 (J2 – J7)
Würth Elektronik 691322310003
(J1)
Würth Elektronik 691322310004 (J2)
Telemetry Power
Board
SiPM Bias Board

## Slide 38
1
6
2
7
4
8
5
9
Chassis
1
6
2
7
4
8
5
9
Chassis
TP
TP
TP
TP
Secondary RTN
+12V
Side of the Box
(P2, P4)
J1 on SiPM Pre-Amp -or- J1 on Charge Pre-Amp Board
Wurth Elektronik
PN: 61800924823
HARTING
PN: 09670150443
Wurth Elektronik
PN: 61800924923
HARTING
PN: 09670150443
Secondary RTN
Secondary RTN
Secondary RTN
+12V
+12V
+12V

## Slide 39
1
6
2
7
3
8
4
9
5
10
14
15
11
12
13
Chassis
1
6
2
7
3
8
4
9
5
10
14
15
11
12
13
Chassis
Cold TPC Charge Pre-Amp PDU Side
T4 Connector on Cold-TPC PDU Box
TEMP Telemetry
-5V Voltage Telem
Telem RTN
Telem RTN
+5V Voltage Telem
-5V Current Telem
Telem RTN
+5 Current Telem
Telem RTN
Enable +
Enable -
TP
TP
TP
TP
TP
TP
Amphenol CONEC
PN: 163A16599X
Amphenol CONEC
PN: 16-001760E
Amphenol CONEC
PN: 164A17009X
Amphenol CONEC
PN: 16-001760E
Telem RTN